## Slide 1: webOS multimedia framework Performance Enhancement

## Slide 2
⑥ 추진배경 / 요구사항정의 | Power Consumption Player and Audio Server Design aligned with Power 중앙 시스템에서의 Power Monitoring 및 측정 복잡한 Power 요소 및 Control 필요함. 최대 Performance 를 유지하면서 Power 감소 User is sure to feel music audio delay to pop out Time latency decrease. Runtime Memory Manage, CPU Management
⑦ 과제 목표 | Low Power and Time Latency Enhancement Low Power Player Design Low Power Audio Server Design Wearable Customization
⑧ 기대 효과 | Power Consumption Less than 20mA competitive to Android No audio drop and glitch Time Latency Less than 700msec from input through kernel device open No user awareness of delay
SW Architecture 과제계획서
요구사항 분석
4월
5월
Architecture Design
9월
구현 및 테스트
11월
① 작성자 | 소속 : SWP연구소 CPS팀 |  | 강명헌 수석 | 
② 작성일 | 2014년 7 월 1 일 | 인증연도 |  | 2012년
③ 과제명 | webOS multimedia framework Performance Enhancement |  |  | 
④ 과제분류* | 2.AD Architecture Design |  |  | 
⑤ 수행 기간 | 2014년 4 월 1 일 ~ 2014년 11 월 29 일 |  |  | 
⑨ 참여 인원 & R&R | Architecture Design : 강명헌 Developer : 최혜진, Kiran
⑩ 추진 세부 일정 | 
⑪ 산출물 (제출용) | SW Architecture Design 문서
⑫ 검증 방법 | 구현된 Power Management를 적용하여 시스템 검증 Time Latency 측정을 통한 before and After 비교 Power 측정을 통한 before and After 비교
⑬ 지원 요청 사항 | 없음
Notes: 상세 과제 계획서에 대해서는 별도의 포멧이 있기 보다는 필요에 따라 3장 이내로 작성하여 제출 가능한 것으로 하면 될 것 같습니다.

## Slide 3: Intro
Terms and Abbreviations
LPA | Low Power Audio
DOU | Daily Of Usage
GStreamer | is the open source, pipeline-based multimedia framework
OpenMax | is the standard API to interface multimedia processing
Audio Server | is to route audio stream to the physical devices, aka PulseAudio for webOS
Audio DSP | is the audio processor to mix and route audio streams in physical
Audio Decoder | is dedicated to decode audio encoded
uMediaServer | manages multiple playbacks requested by applications
Resource Manager | allocates hardware resources to player

## Slide 4: 1. Project Overview
Goal
  To launch wearable watch device over webOS
  To meet power consumption constraint against music playback 
  To achieve short time latency to pop music out 
  Low power audio system
  Low latency audio player
Notes: 15년 3월초를 목표를 개발중이며, 인도인원으로 개발팀이 만들어지게 됩니다.

## Slide 5: 1. Project Overview
webOS Media Framework
  Web-friendly media server
  GStreamer multimedia framework
OpenMax IL Component
Component
Codec
Codec
GStreamer
uMediaServer
OpenMax
(Vender Specific)
Application
Application
Player
Multimedia Framework
uMediaServer
Codec
(Vender Specific )
MediaPlayerService
Stagefright
Starfish media pipeline
OpenMax IL Component
Component
  Android
  webOS
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 6: 1. Project Overview
webOS Audio Framework
  Audio Policy Manager
  Audio Server ( PulseAudio vs. Audio Flinger )
TinyALSA
Audio DSP
Audio DSP
Audio Policy Manager
ALSA
Application
Application
PulseAudio
AudioD
HW Driver
Audio Policy
Audio Flinger
Audio Server
TinyALSA
  Android
  webOS <mobile>
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 7: 1. Project Overview
webOS Media/Audio Architecture
  Media Player feeds decoded stream (PCM) and encoded stream both
  Audio Policy manages sound profiles ( ex Sound, Silent,…)
  Audio Policy manages volume policy against input streams ( ex media, phone, touch, tts,…)
  Audio Policy manages module (ex Phone) and scenario (ex BT device)
  Audio Server set mixer enable/disable and open to feed input streams HW device. < route, ALSA UCM>
WebKit MediaPlayer
Media Player
Gstreamer
uMediaServer
Hardware driver
WebKit
Resource Manager
Pipeline
Manager
uMediaServer
Starfish media pipeline
Audio Server
PulseAudio
Audio DSP
WebKit MediaPlayer
AudioD
Hardware driver
Audio Policy Manager
Audio Flinger
Decoding Processor
Encoded
Stream
PCM
Stream
Audio Decoder
Modules & Scenarios
Web Application
ALSA

## Slide 8: 1. Project Overview
Deliverable
  MP3 playback over BT <NonTunnel>
  MP3 playback over Speaker <Tunnel>
  Startup Latency decreases around 800msec
  Power Consumption decreases down to 28.57mA (+0.57mA compared to Android) over BT
    Total is 58mA, MP3 only is 28mA.
JUN
Initial
2 Pipeline
Player
JUL
gStreamer
Customization
PA 5.0
Applied
SEP
1 Pipeline
Player
SEP 14th
72mA(28.57mA)
1.6sec
0.95sec
2.7sec
AUG
LPA
Applied
OCT 22th
MP3
Consume
Task
NOV30th
Final
OCT 29th
Interim
#1
135mA(65mA)
105mA(43mA)
Time Latency
Power Consumption
0.85sec
89mA(37mA)
NOV 15th
Interim
#2

## Slide 9: 2. Architectural Drivers
Functional Requirements
  128 functional features
    http://collab.lge.com/main/download/attachments/198476541/WebOS+Wearable+Multimedia+Requirement.xls
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 10: 2. Architectural Drivers
Constraints
  Business
    Achieve the higher performance requirements compared to android gear
  Technical
    webOS on ARM v7 with Qualcomm 8x26 SOC
    C/C++, json, python
    Time latency less than 1sec to pop out audio is required
    Power consumption less then 38 mA to consume is required.
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 11: 2. Architectural Drivers
Quality Attributes
  Performance
    LPA module should meet the power consumption less than 20mA proposed by LG MC division.
ID | QA001
Raw Quality Attribute | LPA Performance
Stimulus | Application send the event to start song playback
Source(s) of the stimulus | Applications
Environment | Application initiate to start the playback
Artifact Stimulated | LPA Player
System Response | LPA Player shows its consuming power level via Bluetooth device and speaker
Response Measure(s) | Check whether power consumption is less than 28mA
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 12: 2. Architectural Drivers
Quality Attributes
  Responsibility
    LPA player should pop out audio less than 700ms proposed by MC LG.
ID | QA002
Raw Quality Attribute | LPA Responsibility
Stimulus | Application send the event to start song playback
Source(s) of the stimulus | Applications
Environment | Application initiate to start the playback
Artifact Stimulated | LPA Player
System Response | LPA Player responses to pop out audio via speaker or Bluetooth device
Response Measure(s) | Check whether audio latency to pop out audio is less than 700ms
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 13: 2. Architectural Drivers
Quality Attributes
  Portability
    LPA module should be ported on the any Qualcomm SOC Platform
ID | QA003
Raw Quality Attribute | LPA Portability
Stimulus | Port LPA module on webOS with new Qualcomm SOC Platform
Source(s) of the stimulus | New Qualcomm SOC Platform
Environment | new Mobile Product Development based on webOS
Artifact Stimulated | LPA Code
System Response | LPA works well on webOS with new Qualcomm SOC Platform
Response Measure(s) | Available to check whether module itself can be ported on webOS with new Qualcomm SOC Platform without any modification
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 14: 2. Architectural Drivers
Quality Attributes
  Availability
    LPA module should work even an unexpected faults happens
ID | QA004
Raw Quality Attribute | LPA Availability
Stimulus | Port LPA module on webOS with new Qualcomm SOC Platform
Source(s) of the stimulus | New Qualcomm SOC Platform
Environment | New Mobile Product Development based on webOS
Artifact Stimulated | LPA Code
System Response | LPA works well on webOS with new Qualcomm SOC Platform
Response Measure(s) | check whether module itself can be ported on webOS with new Qualcomm SOC Platform without any modification
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 15: 2. Architectural Drivers
Quality Attributes
  Concurrency
    LPA player should work in multiple playback instance
    LPA player should guarantee concurrency among multiple playbacks
ID | QA005
Raw Quality Attribute | LPA Concurrency
Stimulus | Application send the event to start song playback
Source(s) of the stimulus | Applications
Environment | Application initiate to start the playback
Artifact Stimulated | LPA Player
System Response | LPA Player response to pop out audio via speaker or Bluetooth device
Response Measure(s) | Check whether multiple audio playback work well aligned with Audio Policy
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 16: 2. Architectural Drivers
Quality Attributes Prioritization
ID | Title | Urgency(5) | Difficulty(5) | Evaluation
QA001 | Performance | 5 | 5 | 25
QA002 | Responsibility | 4 | 5 | 20
QA003 | Portability | 5 | 4 | 20
QA004 | Availability | 3 | 4 | 12
QA005 | Concurrency | 3 | 3 | 9
Notes: Open API는 크로녹스 그룹이 배포한 명세에 대한 Wrap API만을 제공한다.
Body는 Vender가 알아서

## Slide 17: 3. System Design
webOS Media/Audio Framework for Latency and Power
  Media player subscription on BT status
  Gstreamer manipulation to feed Compressed and PCM stream.
  Pulseaudio upgrade
  Pulseaudio support ALSA UCM configuration
  Pulseaudio module extension (BSA BT) for NonTunnel mode playback <NonTunnel>
  Pulseaudio module extension (compressed stream) for Tunnel mode playback <Tunnel>
Media Player
Gstreamer
uMediaServer
Hardware driver
Resource Manager
Pipeline
Manager
uMediaServer
Starfish media pipeline
Audio Server
PulseAudio
Audio DSP
WebKit MediaPlayer
AudioD
Hardware driver
Audio Policy Manager
Audio Flinger
Decoding Processor
Compressed
Stream
PCM
Stream
Audio Decoder
Modules & Scenarios
Web Application
ALSA

## Slide 18: 3. System Design
NonTunnel mode
  General audio playback mode
  Audio streams are decoded and fed into Pulseaudio
  Any file playback except MP3 and AAC codec series over Speaker
  Any file playback over BT
Decoder
Element
Audio Decoder
Media Player
Hardware driver
Starfish media pipeline
Source
Element
Demux
Element
Sink
Element
File
PCM
Stream
Audio Server
PulseAudio
Audio DSP
AudioD
Hardware driver
Audio Policy Manager
Audio Flinger
Modules & Scenarios
ALSA Sink
WebKit MediaPlayer
uMediaServer
WebKit
Resource Manager
Pipeline
Manager
uMediaServer
WebKit MediaPlayer
Web Application
GStreamer
Notes:   Audio streams are decoded and fed into Sink that conveys those to Audio Server
  Audio Server receives encoded PCM stream chunks to mix and route

## Slide 19: 3. System Design
Tunnel Mode
  Sleep <play> , Deep Sleep <pause>
  Media player needs to feed compressed stream
  Media player and Pulseaudio needs to synchronize playback time
  Pulseaudio <compressed sink> feeds the compressed stream into Audio DSP.
  Only MP3 and AAC codec series over Speaker
Hardware driver
Source
Element
Demux
Element
Sink
Element
File
Compressed
Stream
Media Player
Starfish media pipeline
WebKit MediaPlayer
uMediaServer
Resource Manager
Pipeline
Manager
uMediaServer
WebKit MediaPlayer
Web Application
GStreamer
Audio Server
PulseAudio
Audio DSP
AudioD
Hardware driver
Audio Policy Manager
Audio Flinger
Modules & Scenarios
Compressed Sink
Decoding Processor

## Slide 20: 4. Architectural Design
2 Players
  Android
  When a application starts or when mode change is required
  2 Players own GStreamer framework per each
    Week point #1 : 2 players spend 1.5 times in memory usage
    Week point #2 : Latency over 3 sec to start playback when after touch
    Week point #3 : Latency over 2 seconds to start playback when required switching mode
PCM
Stream
Audio Decoder
Media Player
Tunnel
WebKit MediaPlayer
uMediaServer
Resource Manager
Pipeline
Manager
uMediaServer
WebKit MediaPlayer
Web Application
Media Player
NonTunnel
Audio Server
PulseAudio
Audio DSP
AudioD
Hardware driver
Audio Policy Manager
Audio Flinger
Modules & Scenarios
Compressed Sink
Decoding Processor
Players
Hardware driver
Compressed
Stream

## Slide 21: 4. Architectural Design
Single Player
  ipelines
  A player is created with 1 pipeline
  When mode change required, player finalizes previous one pipeline and set up new one.
    Week point #1 Latency over 2 seconds to start playback when required switching mode.
PCM
Stream
Audio Decoder
Media Player
WebKit MediaPlayer
uMediaServer
Resource Manager
Pipeline
Manager
uMediaServer
WebKit MediaPlayer
Web Application
Audio Server
PulseAudio
Audio DSP
AudioD
Hardware driver
Audio Policy Manager
Audio Flinger
Modules & Scenarios
Compressed Sink
Decoding Processor
Player
Hardware driver
Compressed
Stream
Gstreamer Pipeline Tunnel
Gstreamer Pipeline NonTunnel
  2 GStreamer pipelines

## Slide 22: 4. Architectural Design
Single Player
  ipelines
  A player is created with 1 pipeline
  Output selector <Tick mode issue>, Dynamic Linking/Unlinking
PCM
Stream
Audio Decoder
Media Player
WebKit MediaPlayer
uMediaServer
Resource Manager
Pipeline
Manager
uMediaServer
WebKit MediaPlayer
Web Application
Audio Server
PulseAudio
Audio DSP
AudioD
Hardware driver
Audio Policy Manager
Audio Flinger
Modules & Scenarios
Compressed Sink
Decoding Processor
Player
Hardware driver
Compressed
Stream
Gstreamer Pipeline
  Single GStreamer pipelines

## Slide 23: 5. Detailed Design
Media Player
  GStreamer - Dynamic linking & unlinking elements
    One media pipeline can work both in the NonTunnel mode and Tunnel mode.
    Parser elements can select Decoder Element or Pulsesink Element to feed audio stream based on its stream type.
Pulsesink
Element
Demux
Element
Source
Element
Media Player
GStreamer Pipeline
uMediaServer
Web Application
Parser
Element
Non-Tunnel
Tunnel
Decoder
Element
ALSA
Audio DSP
module-alsa-sink
module-tiny-compress
PulseAudio

## Slide 24: 5. Detailed Design
Audio Server
  Pulseaudio – Compressed Stream
    Pulseaudio upgrade to handle compressed stream
    Compressed stream feeder module.
Pulsesink
Element
Demux
Element
Source
Element
Media Player
GStreamer Pipeline
uMediaServer
Web Application
Parser
Element
Non-Tunnel
Tunnel
Decoder
Element
ALSA
Audio DSP
module-alsa-sink
module-tiny-compress
PulseAudio

## Slide 25: 5. Detailed Design
Media/Audio framework
  Android KitKat
Pulsesink
Element
Demux
Element
Source
Element
Media Player
uMediaServer
Application
Decoder
Element
Audiod
Application
Using PCM
PCM
Source
PulseAudio
Demux
Element
Source
Element
< Non-Tunnel >
< Tunnel >
module-palm-policy
PCM
Stream
PCM data
ALSA
Audio DSP
module-alsa-sink
module-Bluetooth-device
Bluz
Broadcom
module-Bluetooth-device
Modem
HW 0:9
Physical Back
Speaker Port
HW 0:15
UCM
Physical Front
Speaker Port
HW 0:17
PCM sink
A2DP sink
Physical BT Device
module-tiny-compress
HW 0:9
DEC
SCO
Control Event
PCM Audio Stream
IPC
ES Audio Stream
Socket
Compressed
Stream
Compressed
Stream
Notes:     Week point #1 PulseAudio should be added the implementation to handle Encoded Stream.
    Strong point #1 Power consumption lowers less than the design based on Android Jellybean.

## Slide 26: 5. Detailed Design
Obsolete alternative
  Audio stream goes into the Audio DSP to decode and then pump up to PulseAudio
    Week point #1 notify to Pulseaudio to set mixer. Architectural workaround
Control Event
PCM Audio Stream
IPC
ES Audio Stream
Socket
Pulsesink
Element
Demux
Element
Source
Element
Media Player
uMediaServer
Application
Decoder
Element
Audiod
Application
Using PCM
PCM
Source
PulseAudio
ALSA
Audio DSP
Demux
Element
Source
Element
< Non-Tunnel >
< Tunnel >
module-palm-policy
module-alsa-sink
module-Bluetooth-device
PCM data
Bluz
Broadcom
module-Bluetooth-device
Modem
HW 0:9
Physical Back
Speaker Port
HW 0:0
UCM
Physical Back
Speaker Port
HW 0:2
PCM sink
A2DP sink
Physical BT Device
Compressed
Stream
PCM
Stream
Feeder
Pump
PCM
Stream

## Slide 27: 6. Performance Enhancement
Time Latency Analysis
  Linux LTTng tool
  Key factors to decrease
    GStreamer Plugins: unnecessary module and type finder (800ms  330ms)
    PulseAudio 5.0 version upgrade and tuning (650ms  160ms)
Category | Action Target | Modules
gStreamer | Reduce gStreamer stack and stream buffer | (starfish-pipeline)
Measurement Tool Adoption | Implement LTTng adaption to get performance status | umediaserver, starfish-pipeline, (pulseaudio)
Mediaserver Restructuring | Reduce overhead of resource management | (umediaserver)
Player Restructuring | Implement player with 1 pipeline having output selector | (starfish-pipeline)
Pluseaudio Tunning | Tune queue management to feed encoded streaming | (pulseaudio)
1) an open source tracing framework for Linux
Notes: Element를 통해 Property를 전달합니다. 그런데 다음 Element에서 Input을 인지하여 연결됩니다.
외부Event에 대한 각 Element가 동기화를 이룹니다.

## Slide 28: 6. Performance Enhancement
Power Consumption Analysis
  CPU Occupation
  Linux Perf Tool
  Key factors to decrease
    uMediaServer : LUNA System Bus
    Media Player : I/O interaction, decoder changing
    PulseAudio : Mutex based Audio Stream Feeding
uMediaServer
0.60% umediaserver: 671 umediaserver libc-2.17.so [.] 0x00071f34
0.25% umediaserver: 671 umediaserver libyajl.so.1.0.12 [.] 0x000020b8
0.21% umediaserver: 671 umediaserver libc-2.17.so [.] __libc_calloc
0.21% umediaserver: 671 umediaserver libglib-2.0.so.0.3400.3 [.] 0x000338e4
Media Player
2.41% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] synth_full
1.85% starfish-media-: 9487 starfish-media- [kernel.kallsyms] [k] __copy_to_user_std
1.25% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] III_imdct_l
1.23% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] III_decode
0.98% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] dct32
0.65% starfish-media-: 9487 starfish-media- [kernel.kallsyms] [k] _raw_spin_unlock_irqrestore
0.36% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] III_overlap
0.36% starfish-media-: 9487 starfish-media- libgstmad.so [.] gst_mad_handle_frame
0.35% starfish-media-: 9487 starfish-media- libc-2.17.so [.] 0x00071520
0.32% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] III_aliasreduce
0.24% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] fastsdct
0.21% starfish-media-: 9487 starfish-media- libc-2.17.so [.] memcpy
0.19% starfish-media-: 9487 starfish-media- libmad.so.0.2.1 [.] mad_bit_read
0.17% starfish-media-: 9487 starfish-media- libpthread-2.17.so [.] 0x0000a200
PulseAudio
Spin Lock/ Unlock
1.72% pulseaudio: 1013 pulseaudio [kernel.kallsyms] [k] _raw_spin_unlock_irqrestore
0.67% pulseaudio: 1013 pulseaudio [kernel.kallsyms] [k] fget_light
0.46% pulseaudio: 1013 pulseaudio libpulsecommon-5.0.so [.] 0x00034b06
0.36% pulseaudio: 1013 pulseaudio [kernel.kallsyms] [k] _raw_spin_unlock_irq
0.36% pulseaudio: 1013 pulseaudio [kernel.kallsyms] [k] fput
0.31% pulseaudio: 1013 pulseaudio [kernel.kallsyms] [k] do_sys_poll
0.31% pulseaudio: 1013 pulseaudio [kernel.kallsyms] [k] sub_preempt_count
0.22% pulseaudio: 1013 pulseaudio libpulsecore-5.0.so [.] pa_sconv_s32le_to_s16ne
0.20% pulseaudio: 1013 pulseaudio libpulsecore-5.0.so [.] 0x00022dca
0.17% pulseaudio: 1013 pulseaudio [kernel.kallsyms] [k] eventfd_poll
Notes: Element를 통해 Property를 전달합니다. 그런데 다음 Element에서 Input을 인지하여 연결됩니다.
외부Event에 대한 각 Element가 동기화를 이룹니다.

## Slide 29: 6. Performance Enhancement
Power Consumption Activities
  MP3 playback via BT
  Tasks
    http://collab.lge.com/main/download/attachments/198476541/BT+MP3+Power+Consumption+Detail+Activities_20141130.xlsx
Category | Contents
Audio Decoder | - Adopt Android MP3 Decoder - Modify 16bit audio output
 | - Integer based Vorbis Decoder - Modify 16bit audio output
 | - Integrate HW OMX AAC Decoder - Modify 16bit audio output
 | - Remove Floating Point calculation
PulseAudio | - UIPC_Available making additional spin lock/unlock was removed
 | - Feeding buffer to BSA increase from 20KByte to 200KByte
uMediaServer | - System Event Period Decrease from 200msec to 400msec
 | - Remove PmLog code
Audiod | - When it goes into the sleep mode, NACK response fails to retry to connect so frequent was fixed

## Slide 30: 6. Performance Enhancement
Power Consumption Result
  28.57mA for MP3 Playback which is more than 0.57mA compared to Android KitKat as of Nov 30th
    Target : Total consumption is 65mA, MP3 playback is 28mA.
Chart: 
| #188 | #194 | #199 | #199(개선) | #218(High) | #218(Low)
목표 | 65 | 65 | 65 | 65 | 65 | 65
Total | 135 | 110 | 94.98 | 89 | 83.78 | 72.54
Chart: 
| #188 | #194 | #199 | #199(개선) | #218(High) | #218(Low)
목표 | 28 | 28 | 28 | 28 | 28 | 28
Multimedia | 47 | 29.5 | 31.28 | 36.96 | 34.69 | 28.57
Chart: 
| #188 | #194 | #199 | #199(개선) | #218(High) | #218(Low)
목표 | 12 | 12 | 12 | 12 | 12 | 12
BT | 32 | 27.92 | 17.85 | 21.3 | 20.69 | 14.95
Before/After CPU IDLE Enhancement
+7.5mA
+70mA
Total
Multimedia
BT

## Slide 31: Appendix
webOS Wearable Architecture

## Slide 32: Appendix
Android KitKat Design

## Slide 33: Appendix
Audio System
  PuluseAudio handles Audio Stream
  DASS for TV handle TV and Media audio Stream directly
Audiod
HW Driver
Audiod
BSP Interface
<UCM>
HW Driver
PulseAudio
Audiod
HW Driver
DASS
ALSA
ALSA
webOS Mobile
webOS TV
Open webOS
PulseAudio
ALSA
PulseAudio